## Slide 1: SIPREC Requirements for Media Recording using SIP
IETF Interim meeting 22 Jun 2010
Ken Rehor
on behalf of the team
Draft authors: K. Rehor, A. Hutton, L. Portman, R. Jain, H. Lum

## Slide 2: Agenda (Next Steps from ‘77)
Refine current requirements
Address Open Issues and Public Comments
Describe additional use cases
Publish revised draft
  Target May / Jun 2010
    http://tools.ietf.org/html/draft-rehor-siprec-req-01 May 20, 2010

## Slide 3: Open Issues
Failure modes and handling
Media / codec negotiation
  At setup time
  Mid-call, e.g. during transfers of participants
Network mixing, transcoding
Participant Notification
  Before recording begins, via tone injection, etc.
Privacy Control
Metadata transport

## Slide 4: Use Case 8 Geographically distributed or centralized recording
Remove text for “conference based solution”
 We do not want to limit architectures in requirements doc
Supported by discussion on mailing list

## Slide 5: Use Case 12 real-time media processing
Separate streams for each speaker is highly desired
  Speaker-separated audio supports higher quality speech processing
  But doesn’t imply or require real-time stream
Add specific requirement to support real-time analytics
Suggestions:
  Add specific requirement to enable real-time streaming
  Clarify that REQ-012, -013, -014

## Slide 6: Use Case 12 real-time media processing
New proposed REQ-xxx “The mechanism MUST support separated real-time audio streams.”
Use case: real-time speech analytics
  Must this be specific to speech?
  Where does the real-time stream need to originate? SRC or SRS? Both?

## Slide 7: Revised REQ-012, -013, -014
REQ-012 The mechanism MUST support the ability for an SRC to deliver mixed audio streams from multiple Communication Sessions to an SRS.
REQ-012bis: The mechanism MUST support the ability for an SRC to deliver mixed audio streams from different parties of a given Communication Session to an SRS.
http://www.ietf.org/mail-archive/web/siprec/current/msg00359.html

## Slide 8: Revised REQ-012, -013, -014
REQ-013 The mechanism MUST support the ability to deliver multiple media for a given Communication Session over separate Recording Sessions to the SRS.
REQ-013bis The mechanism MUST support the ability to deliver media from different parties in a given Communication Session over separate Recording Sessions to the SRS.

## Slide 9: Revised REQ-012, -013, -014
REQ-014 The mechanism MUST support the ability to deliver multiple media for a given Communication Session over a single Recording Session to the SRS.
REQ-014bis The mechanism MUST support the ability to deliver media from different parties in a given Communication Session over a single Recording Session to the SRS.
http://www.ietf.org/mail-archive/web/siprec/current/msg00346.html

## Slide 10: Use Case 10: High Availability
Covers situation where SRS fails
  At call setup or during a call
Does not ensure ‘no loss of recording’ situation
  Continuation of recording on a different SRS
Rename Use Case 10 to “Handling SRS Failure”
Add new use case for “Handling SRC failure”
  e.g. failover to secondary SRC
Add new use case for ‘no loss of recording’
  e.g. redundant SRSs or redundant SRCs with SRSs

## Slide 11: Next Steps
Resolve any remaining Open Issues and Public Comments
Publish (hopefully) final draft
  June / July 2010

## Slide 12: Discussion